## Slide 1: Seasonal to Interannual Variability in Phytoplankton Biomass and Diversity on the New England Shelf
Heidi M. Sosik Hui Feng
In Situ Time Series for Validation and Exploration
of Remote Sensing Algorithms
Woods Hole
Oceanographic Institution
University of
New Hampshire

## Slide 2: Project Overview
Goal: Use unique time series to evaluate algorithms that extend MODIS ocean color data beyond chlorophyll to functional type or size-class-dependent phytoplankton retrievals
Approach: End-to-end time series observations, with step-by-step algorithm evaluation and error analysis
single cells  phytoplankton community  bulk water optical properties  sea surface optical properties (air and water)  MODIS optical properties
Martha’s Vineyard Coastal Observatory
Tower mounted
AERONET-OC
MODIS products
Submersible Imaging
Flow Cytometry

## Slide 3: Talk Overview
Phytoplankton Observations
  Single cells to communities
  Biomass, size- and taxon-resolved
Phytoplankton Algorithms
  Absorption spectral shape  size structure
  Diagnostic pigments  size structure
Next Steps

## Slide 4
FlowCytobot
Imaging FlowCytobot
Observing Phytoplankton at MVCO
Martha’s Vineyard Coastal Observatory (MVCO)
Cabled site with power and two-way communications
Microplankton
Picoplankton
Laser-based flow cytometry
Fluorescence and light scattering
Flow cytometry
with video imaging
Automated features for extended deployment (>6 months)
Enumeration, identification, and cell sizing
Thousands of individual cells every hour
Olson et al. 2003
Olson & Sosik 2007

## Slide 5: Single Cells to Biomass
FlowCytobot
Picoplankton
Imaging
FlowCytobot
Microplankton
Light scattering
Cell volume (mm3)
Sosik and Olson 2007
Moberg & Sosik 2012
Olson et al. 2003
Volume from laser scattering
Volume from image analysis
new “distance map” approach
Menden-Deuer
and Lessard 2000

## Slide 6: Single Cells to Communities
Individual cells  Taxa  Communities
Individual cells  Size-classes  Communities
Syn
Notes: http://ifcb-data.whoi.edu/mvco/IFCB5_2012_024_204912_02967.png

## Slide 7: Phytoplankton Algorithms
Spectral absorption shape  size structure
Ciotti et al. 2002
Ciotti and Bricaud 2006

## Slide 8: Phytoplankton Algorithms
FCM C-budget
Spectral absorption shape  size structure
Ciotti et al. 2002
Ciotti and Bricaud 2006

## Slide 9: Phytoplankton Algorithms
Diagnostic pigments  size structure
Vidussi et al. 2001
Uitz et al. 2006
Hirata et al. 2008
Devred et al. 2011
Fraction micro = ( P1,w + P2,w) / ∑Pi,w
Fraction nano = ( P3,w + P4,w + P5,w) / ∑Pi,w
Fraction pico = ( P6,w + P7,w) / ∑Pi,w
P1 = fucoxanthin
P2 = peridinin
…
Microphytoplankton

## Slide 10: Phytoplankton Algorithms
Diagnostic pigments  size structure
P1 = fucoxanthin
P2 = peridinin
…
Picophytoplankton
Fraction micro = ( P1,w + P2,w) / ∑Pi,w
Fraction nano = ( P3,w + P4,w + P5,w) / ∑Pi,w
Fraction pico = ( P6,w + P7,w) / ∑Pi,w
Vidussi et al. 2001
Uitz et al. 2006
Hirata et al. 2008
Devred et al. 2011

## Slide 11: Work in Progress and Next Steps
Water-leaving radiance and aerosol property retrievals
AERONET-OC vs. MODIS
Inherent optical property retrievals
AERONET-OC vs. in situ samples
Diagnostic pigment retrievals
AERONET-OC vs. in situ samples
Phytoplankton carbon retrievals
MODIS vs. cell-based C budgets
Diagnostic pigment algorithm evaluation
HPLC-CHEMTAX vs. cell-based C budgets
Quantification of biases and uncertainties

## Slide 12: Phytoplankton Algorithms
Diagnostic pigments  size structure
Vidussi et al. 2001
Uitz et al. 2006
Devred et al. 2011
Hirata et al. 2008
P1 = fucoxanthin
P2 = peridinin
…
Nanophytoplankton
Fraction micro = ( P1,w + P2,w) / ∑Pi,w
Fraction nano = ( P3,w + P4,w + P5,w) / ∑Pi,w
Fraction pico = ( P6,w + P7,w) / ∑Pi,w