## Slide 1
NASA Carbon Monitoring System
Forest Biomass Pilot Project
National Forest Biomass Effort:
JPL – Ames
Local Forest Biomass Effort:
GSFC-UMD-USFS
Parker Tract, North Carolina
Community Forum
October 5, 2011
Alexandria, Virginia

## Slide 2
SRTM
LANDSAT
ICESat
MODIS
ALOS PALSAR
Satellite and In Situ Observations
USDA FS, FIA Data
Airborne Lidar

## Slide 3: Roles of National and Local Mapping
National Biomass @1-100 ha
Local Biomass @ 1 ha
Geospatial distribution of C stocks
Continental “bottom up” flux calculations
Comparison with atmospheric inversions
Validation of national mapping
Prototype project/county MRV
Ecological controls on C sequestration
USFS FIA data (sample)
National reporting of US C stocks
validation
training, validation
Increasing Geospatial Detail

## Slide 4: Local Mapping
NASA GSFC:
Compton Tucker
Jeff Masek
Bruce Cook
Lola Fatyombo
Forrest Hall
Chris Neigh
University of Maryland:
Ralph Dubayah
George Hurtt
Chengquan Huang
Naira Pinto
Jackie Rosette
Juan Suarez
US Forest Service:
Richard Birdsey
Yude Pan

## Slide 5: Study Sites (Year 1)
Bartlett/Hubbard Brook, New Hampshire (Mixed hardwood w/strong elevation and climate gradients)
  DESDynI Field Study SF lidar (2009)
  USFS Landscape monitoring site; dense historical plot network
Parker Tract, North Carolina (Even-aged Loblolly Pine)
  USFS SF lidar (2005), Photon Counting lidar (Oct 2010), G-LiHT SF lidar (Summer 2011)
  USFS Landscape monitoring site; well characterized biomass & treatment history
Anne Arundel & Howard County MD (mixed hardwood/softwood; suburban)
  SF lidar (2005), Photon Counting (Feb/June 2011 @ Jug Bay)
  UMD field campaigns during winter 2010-11 to collect FIA-style plot data
  Dense plot network at Jug Bay
  Comparison with county-level estimates from FIA
4) Garcia Track, Mendicino County CA (recovering coastal Redwood/Doug Fir)
  SF lidar surveys 2005 and 2009; reflight in 2011
  Carbon credits awarded through Climate Action Reserve (CAR) program

## Slide 6: Field Measurements
  Sites chosen to represent range of stand types, ages
  Flux towers & high density of FIA plots
  Field measurements collected by NCSU and Weyerhaeuser
  7 m diameter, fixed-radius plots (n ≈ 100)
  Species, dbh, live/dead for trees ≥2.54 cm
  Biomass calculated using Jenkins equations
Parker Tract, NC

## Slide 7: CMS-Biomass Data Processing
Field plot data:
Collection
Input
Airborne Lidar data:
- Separate ground/feature returns
- Compute metrics
Radar:
Process ALOS
Forest/Non-Forest mask
Other data sources:
Landsat reflectances (Chris)
Landsat disturbance products(Chris/Chengquan)
NLCD/Enhanced NLCD (Img Tree)
Site boundaries (Naiara)
Create layer stack and extract plot data
Modeling, validation and error analysis
Prediction
Mapping
Error Analysis
Compute biomass
Plot coordinates
DBH, species, live/dead

## Slide 8: Forest Biomass (Maryland)
PRESS RMSE = 48.86 Mg/ha

## Slide 9: Landsat Disturbance

## Slide 10: Growth rates from Landsat-LiDAR data
Year since last disturbance (Landsat)
Canopy height (LiDAR), m
35
30
25
20
15
10
5
0
Parker Track, NC
Vertical growth rates can be estimated by combining LiDAR-derived canopy heights with Landsat disturbance history (Dolan et al., JGR, 2009).
undisturbed

## Slide 11
National Biomass Pilot Project
Project Domain
Center Leads:
Sassan Saatchi (JPL)
Rama Nemani (ARC)
Cook, Masek & Tucker (GSFC)
Co-investigators:
Richard Birdsey (USDA/FS)
Michael Lefsky (CSU)
Estimating Biomass and Carbon Storage by Combining
Satellite and Ground Observations

## Slide 12: National Data Processing
NASA Earth Exchange: Collaborative Computing

## Slide 13
250-m LAI derived from MODIS
MODIS monthly LAI Mosaic is provided at 250 m resolution
Three years (2004-2006) of MODIS data were processed to improve image quality
LAI estimation was implemented using the NLCD land cover map.

## Slide 14
Lorey’s Height Predicting Forest Biomass
(Lefsky et al., 2010)
ICESAT GLAS Forest Height Metric

## Slide 15: From acquisition to image mosaic
ALOS PALSAR acquires data
JAXA EORC processes special K&C slant range image strips
  Thousands of km long, rather than image frames typically created
  Reduced resolution dual pol data (~50m)
Next, orthorectify the data using the SRTM DEM, and apply radiometric corrections if necessary
  Including radiometric terrain correction
Assemble orthorectified images into image mosaics
396 Image Strips
31 UTM tiles, 6x 8 deg in size

## Slide 16: Spatial Biomass Estimator
Parametric Models:
  Multivariate Regressions:
  AGB = f (VI, SAR, SRTM)
Non Parametric Models:
  Coloring by numbers (use of land cover maps)
  Image Segmentation Approach (Lefsky et al., 2010; Mitchard et al., 2011)
  Decision Rule, Random Forest (Saatchi et al., 2007; Kellndorfer et al., 2010)
  Maximum Entropy Approach (Saatchi et al., PNAS 2011)

## Slide 17: Maximum Entropy Model
Maximum Entropy Estimation Model
1. A probabilistic framework
Develop incomplete empirical probability
distribution based on the occurrences
Approximate with a probability distribution of
maximum entropy
Use environmental variables as constraints
A rule classifier to produce forest biomass map
Statistical Model Biomass Estimator
Integrative Approach to Map Biomass (Cont.)
Sample Probability Space

## Slide 18
Preliminary Aboveground National Biomass Map

## Slide 19
AGB Prediction Uncertainty
AGB Prediction
Uncertainty (±%)
Potential Validation Sites